## Slide 1: Control

## Slide 2: Motion Control (kinematic control) for mobile platform
The objective of a kinematic controller is to follow a trajectory described by its position and/or velocity profiles as function of time.
Motion control is not straight forward because mobile robots are typically non-holonomic systems.
However, it has been studied by various research groups and some adequate solutions for (kinematic) motion control of a mobile robot system are available.
Most controllers are not considering the dynamics of the system

## Slide 3: Motion Control: Open Loop Control
trajectory (path) divided in motion segments of clearly defined shape:
  straight lines and segments of a circle.
control problem:
  pre-compute a smooth trajectory based on line and circle segments
Disadvantages:
  It is not at all an easy task to pre-compute a feasible trajectory
  limitations and constraints of the robots velocities and accelerations
  does not adapt or correct the trajectory if dynamical changes of the environment occur.
  The resulting trajectories are usually not smooth

## Slide 4: Motion Control: Feedback Control!
• Set intermediate positions lying on the requested path !
• Given a goal how to compute the control commands for moving on the path !
• Linear and angular velocities to reach the desired configuration!

## Slide 5: Loops
Open loop
current state + model
= resulting position
Closed loop
current state + model
feedback

## Slide 6: Microwave
Cold Food
90 secs
on high
Hot Food

## Slide 7: Smart Microwave
Popcorn Kernels
Apply heat
Is steam?
Popped
Popcorn
No
Yes

## Slide 8: Control System
Actuators
Physical System
Sensors
Controller
Feedback
Actions
Movement
New World
NOISE
NOISE

## Slide 9: A Simple System
Robot state: x
Desired state: x'
Error = (x-x')2
Action: u
Goal: Reach error =0

## Slide 10: Bang Bang Controller
Action in direction of error
error = x-x'
If e<0, u=on
If e>0, u=off

## Slide 11: Proportional Control
Action proportional to error
u = -Kpe + p0
Kp=Proportional gain
p0 = Output with zero error

## Slide 12: Ballcock
José Antonio de Alzate y Ramírez,
Mexican priest and scientist -1790

## Slide 13: Proportional Control - Kp
Notes: The proportional term produces an output value that is proportional to the current error value. Constant Kp, is the proportional gain constant.
High proportional gain results in a large change in the output for a given change in the error. If the proportional gain is too high, the system can become unstable
a small gain results a less responsive or less sensitive controller. If the proportional gain is too low, the control action may be too small when responding to system disturbances.
In a real system, proportional-only control will leave an offset error in the final steady-state condition. Integral action is required to eliminate this error.

## Slide 14: Integral Control
Actions proportional to magnitude and duration of error
Ki ∫e(t)dt
Notes: The integral term accelerates the movement of the process towards the setpoint and eliminates the residual steady-state error that occurs with a pure proportional controller. However, since the integral term responds to accumulated errors from the past, it can cause the present value to overshoot the setpoint value.

## Slide 15: Derivative Control
Actions considering future overshooting
u = -Kpe(t) - Kd e'(t)
"Pull less when
heading in the
right direction"
Notes: Derivative action predicts system behavior and thus improves settling time and stability of the system.

## Slide 16: PID Controller
u = -Kpe(t) - Ki ∫e(t)dt - Kde'(t)

## Slide 17
Damping:
Overdamped
The system returns (exponentially decays) to equilibrium without oscillating.
Critically damped
The system returns to equilibrium as quickly as possible without oscillating.
Underdamped
The system oscillates (at reduced frequency with the amplitude gradually decreasing to zero.
Some terminology

## Slide 18: Transient response (behavior of system in response to transition of one stable state to another)
Td delay time: time required to reach 50 % of target
Ts settling time: time required to achieve and maintain ± 5 % of the target
Tp peak time: time at which the largest value above target is reached
M peak overshoot : largest value above target

## Slide 19: Transient response cont’ed
Steady state error: the system’s percent of error in the limit
Rise time: the time taken to change from a specified low value to a specified high value (usually 10% and 90%) of the output
A system is stable, if its response to a bounded input
is itself bounded.

## Slide 20: Effects of increasing a parameter
Parameter | Rise time | Overshoot | Settling time | Steady-state error | Stability
Kp | Decrease | Increase | Small change | Decrease | Degrade
Ki | Decrease | Increase | Increase | Eliminate | Degrade
Kd | Minor change | Decrease | Decrease | No effect in theory | Improve if small
https://en.wikipedia.org/wiki/PID_controller
(demo of effects of varying PID parameters on the step response of a system)
http://diydrones.com/page/pid-tuning-demos

## Slide 21: Basic issues for designing control systems
Linear dynamical system:
System state equations
X set of states of the system and the environment.
• Y set of outputs. Information available to the controller, since the information about the entire state is often not available to the controller.
• U set of control actions.
For the robot control problem y(t) = x(t)
Output equations

## Slide 22: Basic issues for designing control systems
Controllability:
In set point regulation problem the objective is to achieve and obtain a particular state (or set of states) starting from any initial state.
Can we reach the target set points or any target set points from the initial state ?
Observability
Is it possible to observe state x(t0) by observing y(t) for t0 < t < t1
Stability
Small changes in input or initial conditions do not result in large changes in system behavior.
Asymptotically stable: the variables of an asymptotically stable control system always decrease from their initial value and do not show permanent oscillations

## Slide 23: Motion Control (kinematic control) for mobile platform
The objective of a kinematic controller is to follow a trajectory described by its position and/or velocity profiles as function of time.
Motion control is not straight forward because mobile robots are typically non-holonomic systems.
However, it has been studied by various research groups and some adequate solutions for (kinematic) motion control of a mobile robot system are available.
Most controllers are not considering the dynamics of the system

## Slide 24: Motion Control: Open Loop Control
trajectory (path) divided in motion segments of clearly defined shape:
  straight lines and segments of a circle.
control problem:
  pre-compute a smooth trajectory based on line and circle segments
Disadvantages:
  It is not at all an easy task to pre-compute a feasible trajectory
  limitations and constraints of the robots velocities and accelerations
  does not adapt or correct the trajectory if dynamical changes of the environment occur.
  The resulting trajectories are usually not smooth

## Slide 25: Motion Control: Feedback Control!
• Set intermediate positions lying on the requested path.
• Given a goal how to compute the control commands for
linear and angular velocities to reach the desired configuration!

## Slide 26
Given arbitrary position and orientation of the robot [x, y,θ]
how to reach desired goal orientation and position [xg , yg,θg ]
Problem statement

## Slide 27: Motion Control: Feedback Control, Problem Statement
Find a control matrix K, if exists with kij=k(t,e)
such that the control of v(t) and w(t)
drives the error e to zero.

## Slide 28: Motion Control: Kinematic Position Control
Dy
The kinematics of a differential drive mobile robot described in the initial frame {xI, yI, q} is given by,
where and are the linear velocities in the direction of the xI and yI of the initial frame.
Let α denote the angle between the xR axis of the robots reference frame and the vector connecting the center of the axle of the wheels with the final position.
We set the goal at the
origin of the inertial frame

## Slide 29: Kinematic Position Control: Coordinates Transformation
Dy
Coordinates transformation into polar coordinates with its origin at goal position:
System description in new polar coordinates
For α
for

## Slide 30: Kinematic Position Control: Remarks
The coordinates transformation is not defined at x = y = 0; as in such a point the determinant of the Jacobian matrix of the transformation is not defined, i.e. it is unbounded
For the forward direction of the robot points toward the goal, for it is the backward direction.
By properly defining the forward direction of the robot at its initial configuration, it is always possible to have at t=0. However this does not mean that a remains in I1 for all time t.
Dy

## Slide 31: Kinematic Position Control: The Control Law
It can be shown, that with the feedback controlled system will drive the robot to
The control signal v has always constant sign,
  the direction of movement is kept positive or negative during movement
  parking maneuver is performed always in the most natural way and without ever inverting its motion.

## Slide 32: Kinematic Position Control: Resulting Path
The goal is in the center and the initial position on the circle.

## Slide 33: Kinematic Position Control: Stability Issue
It can further be shown, that the closed loop control system is locally exponentially stable if
Proof: linearize around the center, compute eigenvalues for small x -> cosx = 1, sinx = x
and the characteristic polynomial of the matrix A of all roots have negative real parts.