## Slide 1: Filters (Smoothing, Edge Detection)

## Slide 2: What is an image?
We can think of an image as a function, f, from R2 to R:
  f( x, y ) gives the intensity at position ( x, y )
  Realistically, we expect the image only to be defined over a rectangle, with a finite range:
    f: [a,b]x[c,d]  [0,1]
A color image is just three functions pasted together. We can write this as a “vector-valued” function:
Notes: As opposed to [0..255]

## Slide 3
Image
Brightness values
I(x,y)

## Slide 4: What is a digital image?
In computer vision we usually operate on digital (discrete) images:
  Sample the 2D space on a regular grid
  Quantize each sample (round to nearest integer)
If our samples are D apart, we can write this as:
f[i ,j] = Quantize{ f(i D, j D) }
The image can now be represented as a matrix of integer values

## Slide 5: Image Processing
An image processing operation typically defines a new image g in terms of an existing image f.
We can transform either the domain or the range of f.
Range transformation:
What kinds of operations can this perform?
Some operations preserve the range but change the domain of f :
What kinds of operations can this perform?
Notes: Use photoshop to make something grayscale

## Slide 6: Filtering and Image Features
Given a noisy image
How do we reduce noise ?
How do we find useful features ?
Filtering
Point-wise operations
Edge detection

## Slide 7: Noise
Image processing is useful for noise reduction...
Common types of noise:
  Salt and pepper noise: contains random occurrences of black and white pixels
  Impulse noise: contains random occurrences of white pixels
  Gaussian noise: variations in intensity drawn from a Gaussian normal distribution
Notes: Salt and pepper and impulse noise can be due to transmission errors (e.g., from deep space probe), dead CCD pixels, specks on lens
We’re going to focus on Gaussian noise first.
If you had a sensor that was a little noisy and measuring the same thing over and over, how would you reduce the noise?

## Slide 8: Practical noise reduction
How can we “smooth” away noise in a single image?
Notes: Replace each pixel with the average of a kxk window around it

## Slide 9: Mean filtering (average over a neighborhood)
Notes: Replace each pixel with the average of a kxk window around it
What happens if we use a larger filter window?

## Slide 10: Effect of mean filters
Notes: Demo with photoshop

## Slide 11: Cross-correlation filtering
Let’s write this down as an equation. Assume the averaging window is (2k+1)x(2k+1):
We can generalize this idea by allowing different weights for different neighboring pixels:
This is called a cross-correlation operation and written:
H is called the “filter,” “kernel,” or “mask.”

## Slide 12: Convolution
A convolution operation is a cross-correlation where the filter is flipped both horizontally and vertically before being applied to the image:
It is written:
Suppose H is a Gaussian or mean kernel. How does convolution differ from cross-correlation?
Notes: They are the same for filters that have both horizontal and vertical symmetry.

## Slide 13
Convolution
MATLAB functions: conv2, filter2, imfilter
F
Convention: kernel is “flipped”
F
G

## Slide 14: Mean kernel
What’s the kernel for a 3x3 mean filter?
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: ones, divide by 9

## Slide 15: Gaussian Filtering
A Gaussian kernel gives less weight to pixels further from the center of the window
This kernel is an approximation of a Gaussian function:
1 | 2 | 1
2 | 4 | 2
1 | 2 | 1

## Slide 16: Gaussian Averaging
Rotationally symmetric.
Weights nearby pixels more than distant ones.
  This makes sense as probabalistic inference.
A Gaussian gives a good model of a fuzzy blob

## Slide 17
An Isotropic Gaussian
The picture shows a smoothing kernel proportional to
(which is a reasonable model of a circularly symmetric fuzzy blob)

## Slide 18: Mean vs. Gaussian filtering

## Slide 19: How big should the mask be?
The std. dev of the Gaussian  determines the amount of smoothing.
The samples should adequately represent a Gaussian
For a 98.76% of the area, we need
m = 5
5.(1/)  2    0.796, m 5
5-tap filter
g[x] = [0.136, 0.6065, 1.00, 0.606, 0.136]

## Slide 20: The size of the mask
Bigger mask:
  more neighbors contribute.
  smaller noise variance of the output.
  bigger noise spread.
  more blurring.
  more expensive to compute.
  In Matlab function conv, conv2

## Slide 21: Gaussian filters
Source: K. Grauman
Remove “high-frequency” components from the image (low-pass filter)
Convolution with self is another Gaussian
  So can smooth with small- kernel, repeat, and get same result as larger- kernel would have
  Convolving two times with Gaussian kernel with std. dev. σ
is same as convolving once with kernel with std.
dev.  2
Separable kernel
  Factors into product of two 1D Gaussians

## Slide 22
Separability of the Gaussian filter
Source: D. Lowe

## Slide 23: Separability example
*
* =
=
2D convolution (center location only)
Source: K. Grauman
The filter factors into a product of 1D filters:
Perform convolution along rows:
Followed by convolution along the remaining column:

## Slide 24
Efficient Implementation
Both, the BOX filter and the Gaussian filter are separable:
  First convolve each row with a 1D filter
  Then convolve each column with a 1D filter.

## Slide 25: Linear Shift-Invariance
A tranform T{} is
Linear if:
T(a g(x,y)+b h(x,y)) = a T{g(x,y)} + b T(h(x,y))
Shift invariant if:
Given T(i(x,y)) = o(x,y)
T{i(x-x0, y- y0)} = o(x-x0, y-y0)

## Slide 26: Median filters
A Median Filter operates over a window by selecting the median intensity in the window.
What advantage does a median filter have over a mean filter?
Is a median filter a kind of convolution?
Median filter is non linear
Notes: Better at salt’n’pepper noise
Not convolution: try a region with 1’s and a 2, and then 1’s and a 3

## Slide 27: Comparison: salt and pepper noise

## Slide 28: Comparison: Gaussian noise

## Slide 29: Edge detection as filtering

## Slide 30: Origin of Edges
Edges are caused by a variety of factors
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity

## Slide 31: Edge detection (1D)
F(x)
x
F ’(x)
x
Edge= sharp variation
Large first derivative

## Slide 32: Edge is Where Change Occurs
Change is measured by derivative in 1D
Biggest change, derivative has maximum magnitude
Or 2nd derivative is zero.

## Slide 33: Image gradient
The gradient of an image:
The gradient points in the direction of most rapid change in intensity
The gradient direction is given by:
  How does this relate to the direction of the edge?
The edge strength is given by the gradient magnitude

## Slide 34: The discrete gradient
How can we differentiate a digital image f[x,y]?
  Option 1: reconstruct a continuous image, then take gradient
  Option 2: take discrete derivative (finite difference)
How would you implement this as a cross-correlation?

## Slide 35: The Sobel operator
Better approximations of the derivatives exist
  The Sobel operators below are very commonly used
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
  The standard defn. of the Sobel operator omits the 1/8 term
    doesn’t make a difference for edge detection
    the 1/8 term is needed to get the right gradient value, however

## Slide 36: Gradient operators
(a): Roberts’ cross operator (b): 3x3 Prewitt operator
(c): Sobel operator (d) 4x4 Prewitt operator

## Slide 37: Effects of noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Where is the edge?

## Slide 38: Solution: smooth first
Where is the edge?
Look for peaks in

## Slide 39: Derivative theorem of convolution
This saves us one operation:

## Slide 40: Derivative of Gaussian filter
Is this filter separable?
* [1 -1] =

## Slide 41: Derivative of Gaussian filter
Which one finds horizontal/vertical edges?
x-direction
y-direction

## Slide 42: Laplacian of Gaussian
Consider
Laplacian of Gaussian
operator
Where is the edge?
Zero-crossings of bottom graph

## Slide 43: 2D edge detection filters
is the Laplacian operator:
Laplacian of Gaussian
Gaussian
derivative of Gaussian

## Slide 44: Tradeoff between smoothing and localization
Smoothed derivative removes noise, but blurs edge. Also finds edges at different “scales”.
1 pixel
3 pixels
7 pixels
Source: D. Forsyth

## Slide 45: Implementation issues
The gradient magnitude is large along a thick “trail” or “ridge,” so how do we identify the actual edge points?
How do we link the edge points to form curves?
Source: D. Forsyth
Notes: Figures show gradient magnitude of zebra at two different scales

## Slide 46: Optimal Edge Detection: Canny
Assume:
  Linear filtering
  Additive iid Gaussian noise
Edge detector should have:
  Good Detection. Filter responds to edge, not noise.
  Good Localization: detected edge near true edge.
  Single Response: one per edge.

## Slide 47: Optimal Edge Detection: Canny (continued)
Optimal Detector is approximately Derivative of Gaussian.
Detection/Localization trade-off
  More smoothing improves detection
  And hurts localization.
This is what you might guess from (detect change) + (remove noise)

## Slide 48: Canny edge detector
Filter image with derivative of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression:
  Thin multi-pixel wide “ridges” down to single pixel width
Linking and thresholding (hysteresis):
  Define two thresholds: low and high
  Use the high threshold to start edge curves and the low threshold to continue them
MATLAB: edge(image, ‘canny’)
Source: D. Lowe, L. Fei-Fei

## Slide 49: The Canny edge detector
original image (Lena)

## Slide 50: The Canny edge detector
norm of the gradient

## Slide 51: The Canny edge detector
thresholding

## Slide 52: The Canny edge detector
thinning
(non-maximum suppression)

## Slide 53: Non-maximum suppression
Check if pixel is local maximum along gradient direction
  requires checking interpolated pixels p and r

## Slide 54
Predicting
the next
edge point
Assume the marked point is an edge point. Then we construct the tangent to the edge curve (which is normal to the gradient at that point) and use this to predict the next points (here either r or s).
(Forsyth & Ponce)

## Slide 55: Hysteresis
Check that maximum value of gradient value is sufficiently large
  drop-outs? use hysteresis
    use a high threshold to start edge curves and a low threshold to continue them.

## Slide 56: Canny Edge Detection (Example)
courtesy of G. Loy
gap is gone
Original image
Strong edges
only
Strong + connected weak edges
Weak edges

## Slide 57: Effect of  (Gaussian kernel size)
Canny with
Canny with
original
The choice of depends on desired behavior
  large detects large scale edges
  small detects fine features

## Slide 58: Scale
(Forsyth & Ponce)
Smoothing
Eliminates noise edges.
Makes edges smoother.
Removes fine detail.
Notes: Figures show gradient magnitude of zebra at two different scales

## Slide 60
fine scale
high
threshold

## Slide 61
coarse
scale,
high
threshold

## Slide 62
coarse
scale
low
threshold

## Slide 63: Scale space (Witkin 83)
Properties of scale space (w/ Gaussian smoothing)
  edge position may shift with increasing scale ()
  two edges may merge with increasing scale
  an edge may not split into two with increasing scale
larger
Gaussian filtered signal
first derivative peaks

## Slide 64
Computer Vision - A Modern
Approach Set: Linear Filters Slides by D.A. Forsyth
Filters are templates
Applying a filter at some point can be seen as taking a dot-product between the image and some vector
Filtering the image is a set of dot products
Insight
filters look like the effects they are intended to find
filters find effects they look like

## Slide 65: Filter Bank
Leung & Malik, Representing and Recognizing the Visual Apperance using 3D Textons, IJCV 2001

## Slide 66: Learning to detect boundaries
Berkeley segmentation database: http://www.eecs.berkeley.edu/Research/Projects/CS/vision/grouping/segbench/
image
human segmentation
gradient magnitude

## Slide 67: pB boundary detector
Figure from Fowlkes
Martin, Fowlkes, Malik 2004: Learning to Detection Natural Boundaries…
http://www.eecs.berkeley.edu/Research/Projects/CS/vision/grouping/papers/mfm-pami-boundary.pdf

## Slide 68: pB Boundary Detector
- Estimate Posterior probability of boundary passing through centre point based on local patch based features
- Using a Supervised Learning based framework

## Slide 69: Results
Human (0.95)
Pb (0.88)

## Slide 70: Results
Human
Pb
Human (0.96)
Global Pb
Pb (0.88)

## Slide 71: Corners contain more edges than lines.
A point on a line is hard to match.
Corner detection

## Slide 72: Corners contain more edges than lines.
A corner is easier

## Slide 73: Edge Detectors Tend to Fail at Corners

## Slide 74: Finding Corners
Intuition:
  Right at corner, gradient is ill defined.
  Near corner, gradient has two different values.

## Slide 75: Formula for Finding Corners
We look at matrix:
Sum over a small region, the hypothetical corner
Gradient with respect to x, times gradient with respect to y
Matrix is symmetric
WHY THIS?

## Slide 76
First, consider case where:
This means all gradients in neighborhood are:
(k,0) or (0, c) or (0, 0) (or off-diagonals cancel).
What is region like if:
l1 = 0?
l2 = 0?
l1 = 0 and l2 = 0?
l1 > 0 and l2 > 0?

## Slide 77: General Case:
From Linear Algebra, it follows that because C is symmetric:
With R a rotation matrix.
So every case is like one on last slide.

## Slide 78: So, to detect corners
Filter image.
Compute magnitude of the gradient everywhere.
We construct C in a window.
Use Linear Algebra to find l1 and l2.
If they are both big, we have a corner.

## Slide 79: Harris Corner Detector - Example